## Slide 1: ECE 2140 SoC Design Lempel-Ziv-Welch (LZW) Compression
SHAUN HOLTZMAN - SHH117@PITT.EDU TRAVIS WISE - TWW12@PITT.EDU
1 min

## Slide 2: LZW Compression Overview
Blocks in our design:
LZW Compression Controller
LZW Compression Dictionary
LZW Compression Dictionary Controller
LZW Compression Dictionary Block
LZW Decompression Software Block
3 min
Universal lossless data compression algorithm
Potential for high throughput in a hardware implementation
Main benefits:
  Represent data with a smaller amount of bits than the original data
  Decompressing exactly represents the original data
  Both compression and decompression can be done using only the default dictionary of the single 255 ASCII characters
  No need to use additional dictionary entries added during compression in order to do decompression

## Slide 3: Compression Flowchart
Start with first byte stored in STRING
Input next next into CHAR
Check if STRING+CHAR in dictionary
  Yes: Make STRING = STRING + CHAR
  No: Output STRING, add STRING+CHAR to dictionary, set STRING=CHAR
Go back to 2 while there is still data to be read
1 min

## Slide 4: Decompression Flowchart
Read in first code into OCODE and translate its output
Read in next code into NCODE
Is NCODE in the dictionary?
  Yes: set STRING = translation of NCODE
  No: set STRING = translation of OCODE + CHAR
Output STRING
Set CHAR = first character in STRING
Add OCODE + CHAR to dictionary
Set OCODE = NCODE
Go back to 2 if there is still data left to be decompressed
1 min

## Slide 5: Simple Compression Example
Original input: 43 characters, 8-bits each
  43x8 = 344 bits
Compressed output: 27 numbers using 8-bits, 8 numbers using 12-bits
  (27x8) + (8x12) = 312 bits
9% less bits used
1 min
Notes: Shaun

## Slide 6: Simple Decompression Example
Decompressed output exactly matches original data that was compressed
Decompression uses the same base dictionary of the 256 ASCII characters
1 min
Notes: Shaun

## Slide 7: Architecture/Model
1 min

## Slide 8: Architecture/Model
2 min

## Slide 9: Schedule and Status
 |  |  |  |  | January |  |  |  | February |  |  |  | March |  |  |  | April |  | 
ID | Task | Who | Status |  | 9 | 16 | 23 | 30 | 6 | 13 | 20 | 27 | 6 | 13 | 20 | 27 | 3 | 10 | 17
1 | S/W Compression | Shaun | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 | S/W Decompression | Shaun | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 | Architectural H/W Design | Travis | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | Architectural S/W Design | Shaun | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 | Testbench | Travis | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 | Dictionary HDL | Shaun | In progress |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 | Toplevel HDL | Travis | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 | Finalizing/Optimizing | Travis | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 | Communicate H/W Compression results with S/W | Shaun | Starting with psuedo data from preset FIFO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 | S/W decoding on Board | Shaun | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 | S/W Decompression on Board | Shaun | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 min

## Slide 10: Schedule and Status
Accomplishments:
  Architectural design complete
  Standalone software implementation complete
Working on this week:
  Starting dictionary HDL
  Starting software block to read in compressed data from h/w FIFO
  Starting dictionary h/w controller
Challenges/Difficulties/Needs
  No major difficulties yet
  Schedule should not slip if we are persistent
2 min

## Slide 11: LZW Compression Controller
Orchestrates whole algorithm
Interfaces between SW and HW
Controls I/O FIFOs and the dictionary search algorithm
1 min

## Slide 12: LZW Compression Dictionary
Top-level module for the dictionary
Contains multiple dictionary blocks in order to parallelize searches
Number of blocks in parallel can be customizable at synthesis-time
2 min

## Slide 13: LZW Compression Dictionary Controller
Coordinates all dictionary blocks
Combines N-bit long vectors into a single std_logic for the top-level
Responsible for maintaining the dictionary length and writing to the dictionary
1 min

## Slide 14: LZW Compression Dictionary Block
Dictionary blocks search through a 20-bit BRAM to find a matching prefix and character entry
If the entry is found in the block, the counter/current address will be used as the new prefix
The controller here is responsible for incrementing the read address and asserting the search_complete signal
2 min

## Slide 15: LZW Decompression Software Block
Reads in compressed data from H/W FIFO
Uses S/W dictionary initialized with 256 base ASCII characters
Recursively decodes compressed data to generate decompressed data
1 min

## Slide 16: LZW Compression Summary - Questions?
 |  |  |  |  | January |  |  |  | February |  |  |  | March |  |  |  | April |  | 
ID | Task | Who | Status |  | 9 | 16 | 23 | 30 | 6 | 13 | 20 | 27 | 6 | 13 | 20 | 27 | 3 | 10 | 17
1 | S/W Compression | Shaun | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 | S/W Decompression | Shaun | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 | Architectural H/W Design | Travis | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | Architectural S/W Design | Shaun | Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 | Testbench | Travis | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 | Dictionary HDL | Shaun | In progress |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 | Toplevel HDL | Travis | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 | Finalizing/Optimizing | Travis | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 | Communicate H/W Compression results with S/W | Shaun | Starting with psuedo data from preset FIFO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 | S/W decoding on Board | Shaun | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 | S/W Decompression on Board | Shaun | Not started |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 min